## Slide 1
Raycasting Ground Truth Protocol
Creating synthetic tunnel data for validation using TLSynth methodology

## Slide 2
TLSynth Scanning Simulation (§3.1-3.5)
TLSynth Pipeline:
1.
§3.1 Scanning Simulation: UV sphere → ray casting → hit positions
2.
§3.2 Noise Model: r_noise = 5mm + 2mm × (distance/10m)
3.
§3.3 Point Deletion: Optional occlusion filtering
4.
§3.4 Color Assignment: RGB from mesh material
5.
§3.5 Export: Save as PLY/LAS format
Notes: TLSynth paper describes complete scanning simulation pipeline. We apply these 5 steps to create synthetic ground truth: 1) Use UV sphere as scanner, 2) Add realistic noise, 3) Handle occlusion, 4) Assign colors, 5) Export to LAS. This ensures our synthetic data matches real LiDAR behavior.

## Slide 3
Three-Phase Protocol
Phase A: T0 Raycast
Clean reference scan
Phase B: Deformation
Inject known changes
Phase C: Tn Raycast
Deformed scan
Validation: Tool measures deformation vs ground truth
Notes: High-level overview: Three phases create synthetic ground truth. Phase A: raycast clean tunnel to get T0. Phase B: modify mesh to inject known deformation. Phase C: raycast modified mesh to get Tn. Finally, load both into tool and validate accuracy.

## Slide 4
Phase A: T0 Raycast (1/2) - Setup
Step 1: Load tunnel mesh
Input: tunnel_lidar_scene.blend (clean mesh)
Tunnel_Lining: 16,100 vertices (smooth surface)
Step 2: Create scanner sphere
Scanner location: (0, 10, 3) meters
Sphere radius: 0.1 m
Subdivisions: 32×16 (512 rays)
Position: 10m along tunnel, 3m height (typical probe location)
Notes: Phase A setup: Load the Blender scene with tunnel geometry. The Tunnel_Lining mesh is our scanning target. Create UV sphere at (0, 10, 3) - this represents scanner position. Each sphere vertex becomes a ray origin. 512 rays total.

## Slide 5
Phase A: T0 Raycast (2/2) - Execute
Step 3: Raycast and export
for each vertex in scanner_sphere:
world_pos = scanner_center + vertex_offset
ray_direction = (world_pos - center).normalized()
hit_loc, hit_dist = raycast(world_pos, ray_dir, tunnel_lining)
if hit:
noise_mm = 5 + (hit_dist / 10) * 2
noisy_point = hit_loc + gaussian(0, noise_mm/1000)
T0_points.append(noisy_point)
export T0_points → T0.las
Output: T0.las (364 points, noise-corrupted clean reference)
Radius (fitted): 3.0000 m
Eccentricity: 0.1 mm
Ovality: 0.05%
Notes: Execute the raycasting: for each vertex on sphere, cast ray from that position toward tunnel. Record hit positions. Add distance-dependent noise (5mm baseline + 2mm per 10m). Export 364 hit points to LAS. T0 is our clean reference with known geometry.

## Slide 6
Phase B: Inject Deformation (1/2)
Define ground truth deformation parameters
Deformation 1 (Crown settlement):
├─ Location: chainage 20 m
├─ Magnitude: -7 mm (downward)
└─ Extent: ±2m gaussian taper
Deformation 2 (Sidewall convergence):
├─ Location: chainage 45 m
├─ Magnitude: -5 mm (inward)
└─ Extent: ±3m gaussian taper
Deformation 3 (Local damage):
├─ Location: chainage 65 m
├─ Magnitude: -15 mm (localized)
└─ Type: point defect
Record in ground_truth.csv for later comparison
Notes: Phase B step 1: Define what deformations you want to introduce. We use 3 example deformations: crown settlement at 20m, sidewall convergence at 45m, local damage at 65m. These represent realistic tunnel deterioration patterns. Document exact values - these are your ground truth.

## Slide 7
Phase B: Inject Deformation (2/2)
Modify Blender mesh
for vertex in tunnel_lining_mesh:
y = vertex.co.y # chainage
# Crown settlement at Y=20m
if 18 < y < 22:
offset = -0.007 * gaussian_taper(y - 20)
vertex.co.z += offset
# Sidewall convergence at Y=45m
if 42 < y < 48:
offset = -0.005 * gaussian_taper(y - 45)
vertex.co.x *= (1 + offset / radius)
vertex.co.y *= (1 + offset / radius)
mesh.update()
save("tunnel_deformed.blend")
Verification: Crown ↓7mm, Width ↓5mm, Mesh valid ✓
Notes: Programmatically modify Blender mesh vertices. For crown settlement: lower Z coordinate at chainage 20m. For convergence: contract X/Y coordinates (move inward) at chainage 45m. Use gaussian tapering so deformation is smooth, not sharp. Save modified mesh as tunnel_deformed.blend.

## Slide 8
Phase C: Tn Raycast (1/2)
Key rule: SAME scanner position as T0
# CRITICAL: Same location, same sphere
scanner_location = (0, 10, 3) # IDENTICAL TO T0
scanner_sphere = UV_Sphere(subdivisions=32x16, location=scanner_location)
# Load DEFORMED mesh (different from T0)
tunnel_mesh = load("tunnel_deformed.blend").Tunnel_Lining
# Raycast (same algorithm as T0)
for vertex in scanner_sphere:
world_pos = scanner_center + vertex_offset
ray_dir = (world_pos - center).normalized()
hit_loc, hit_dist = raycast(world_pos, ray_dir, tunnel_mesh) # NOW: deformed!
if hit:
noise_mm = 5 + (hit_dist / 10) * 2 # SAME noise as T0
noisy_point = hit_loc + gaussian(0, noise_mm/1000)
Tn_points.append(noisy_point)
export Tn_points → Tn.las
Notes: Phase C: Raycast deformed mesh using identical scanner setup. Only difference from T0: target mesh is now deformed. Scanner position, noise model, and ray count must be identical. This ensures differences between T0 and Tn are ONLY from deformation, not from different scanner locations or noise.

## Slide 9
Phase C: Tn Raycast (2/2)
Output: Tn.las (deformed scan)
T0 (Clean)
Radius: 3.0000 m
Eccent: 0.1 mm
Ovality: 0.05%
Points: 364
Tn (Deformed)
Radius: 2.9995 m
Eccent: 1.5 mm
Ovality: 0.08%
Points: 364
Difference (due to deformation):
ΔRadius: -0.5 mm (convergence effect)
ΔEccent: +1.4 mm (asymmetric settlement)
ΔOvality: +0.03% (ovalization from deformation)
Notes: Now we have two synthetic point clouds: T0 clean and Tn deformed. Tn shows measurable changes due to injected deformation. Radius decreased (convergence), eccentricity increased (settlement asymmetry), ovality increased (loss of perfect circle). These are our ground truth changes. Next step: load into tool and measure.

## Slide 10
Validation: Load & Measure
1. Load T0.las into tool → record baseline metrics (R, e, oval)
2. Load Tn.las into tool → measure deformation (Step 6)
3. Tool reports: crown_settle, convergence, local_damage
4. Compare tool output vs ground_truth.csv
5. Calculate error: |measured - prescribed|
6. Assert: error < ±1mm for PASS
✓ If error < ±1mm → Tool is VALIDATED
✗ If error > ±1mm → Debug registration, noise, fitting
Notes: Validation procedure: Load both T0 and Tn into tunnel_analysis tool. Tool extracts geometry from each scan. Tool compares T0 vs Tn and reports deformation metrics. Compare tool output against our ground_truth.csv. If error is small (< 1mm), tool measurement is accurate. If error is large, investigate: registration issues, noise level, fitting algorithm.

## Slide 11
Build Confidence: 4 Validation Scenarios
A
Scenario A: No deformation
T0 → T0 (identity). Expect: error ≈ 0mm.
B
Scenario B: Single metric
Test each: crown-only, convergence-only, damage-only.
C
Scenario C: Combined
All 3 deformations at once (realistic multi-component).
D
Scenario D: Offset scanner
Raycast from different position. Deformation still measurable.
Record all results in validation_results.csv
Notes: Repeat validation with different deformation scenarios. Scenario A: no deformation (tests noise floor). Scenario B: single metric isolated (tests each measurement pipeline). Scenario C: realistic combined deformation (stresses algorithm). Scenario D: different scanner location (tests generalization). Build confidence by passing multiple independent tests.

## Slide 12
Implementation Checklist
[ ] Load tunnel_lidar_scene.blend
[ ] Verify Tunnel_Lining mesh (16,100 verts)
[ ] Setup scanner sphere @ (0, 10, 3)
[ ] Raycast T0 → export T0.las
[ ] Record T0 metadata
[ ] Create deformed mesh (crown, convergence)
[ ] Raycast Tn → export Tn.las
[ ] Load T0, Tn into tool
[ ] Measure deformation metrics
[ ] Compare vs ground_truth.csv
[ ] Calculate error
[ ] Repeat scenarios B, C, D
[ ] Write validation report
[ ] Commit to git
Notes: 14-step checklist to execute the full protocol. Expected time: ~2 hours from start to finish. Critical steps: raycast T0/Tn (identical scanner, different mesh), load into tool, compare measurements. Document every step for reproducibility.

## Slide 13
Summary: TLSynth Protocol
What we create:
• T0.las: Clean reference (364 points, 3.0m radius)
• Tn.las: Deformed scan (known -7mm crown, -5mm convergence)
• ground_truth.csv: Prescribed deformation values
• validation_results.csv: Measured vs ground truth comparison
Outcome: Validate tunnel_analysis tool accuracy (mm-level)
Based on TLSynth paper §3.1-3.5 (Scanning Simulation Pipeline)
Notes: Summary: We create synthetic ground truth by applying TLSynth methodology. Raycast clean mesh → T0. Modify mesh with known deformation → Tn. Load both into tool, measure, compare. If tool accuracy is high (< 1mm error), ready for field validation. If error is high, debug and iterate. This rigorous approach ensures confidence in the measurement pipeline.