## Slide 1
Raycasting Ground Truth Validation
Synthetic LiDAR for Tool Step 6 (M3C2) Verification
2026-06-29

## Slide 2
Initial State (Phase A/B/C v1)
Scripts targeted imaginary tunnel (straight, R=3.0m, 1 scanner, -7/-5/-15mm)
Never actually run end-to-end
Config copy-paste risks ("must match byte-for-byte")
Real dataset blender_lidar_t0t5 is curved (R=500m), 3 TLS stations, progressive T1-T5

## Slide 3
Realign to Real Geometry
Verify .blend via Blender MCP: R=500m curve, radius 4.256m, 3 stations @ arc-len 10/40/70m
Build single engine (raycast_tunnel_epochs.py) for T0 & Tn — same code path, no drift
Deform in local cross-section frame (ground_truth.csv magnitudes: crown -45, side -35, local -40mm @ T5)

## Slide 4
Single Engine, Two Validators
Engine
• tools/raycast_tunnel_epochs.py
• Blender bpy + BVHTree
• T0 clean, Tn deformed
• Same 3 stations & noise
• Export T0-T5 .txt/.json
Validator 1
• phase_c_validate.py
• Window-mean in frame
• Checks raycast fidelity
• Lower bound (bias low)
• Regenerable
Validator 2
• crosscheck_tool_step6.py
• Call Step 6 M3C2 (prod)
• Independent check
• Mm-level accuracy
• FINAL TRUTH

## Slide 5
Validator 1: Window-Mean (Raycast Fidelity)
Epoch | Crown err | Side err | Local err | MAE
T1 | 0.3 | 0.0 | 0.0 | 0.1mm
T2 | 0.2 | 0.0 | 0.0 | 0.1mm
T3 | 0.1 | 0.1 | 2.2 | 0.8mm
T4 | 1.4 | 1.6 | 3.6 | 2.2mm
T5 | 1.9 | 2.3 | 5.5 | 3.2mm
Window-mean is lower bound; narrow features read low

## Slide 6
Validator 2: Tool M3C2 (py4dgeo) — FINAL TRUTH
Epoch | Crown err | Side err | Local err | Peak
T1 | 1.0 | 0.0 | 0.0 | M3C2
T2 | 0.9 | 0.4 | 0.0 | M3C2
T3 | 0.8 | 0.7 | 1.0 | M3C2
T4 | 1.4 | 0.1 | 1.3 | M3C2
T5 | 1.3 | 0.1 | 2.4 | M3C2
Tool recovers GT ≤ 2.4mm peak — mm-level accurate

## Slide 7
Ground Truth by Epoch
Crown Settlement @ 20m
T0: 0 T1: -5 T2: -12 T3: -20 T4: -30 T5: -45 mm
Sidewall Convergence @ 45m
T0: 0 T1: 0 T2: -5 T3: -12 T4: -22 T5: -35 mm
Local Damage @ 65m
T0: 0 T1: 0 T2: 0 T3: -15 T4: -25 T5: -40 mm

## Slide 8
Technical Validation
✓
Geometry verified via Blender MCP inspection (R=500, radius 4.25m, curve centerline)
✓
Path robustness: scripts resolve via __file__ (run from any cwd)
✓
Full series T0-T5 generated (112k-112.5k points/epoch, ~4.2MB each)
✓
Two independent validators (window-mean + tool M3C2)
✓
25MB regenerable point clouds gitignored; metadata/CSV tracked

## Slide 9
Conclusions
Tool Step 6 (py4dgeo M3C2) is mm-level accurate on curved tunnel geometry
Raycasting ground truth validates the measurement pipeline end-to-end
Single engine architecture eliminates config-drift risk
Ready for next phase: higher ray density (0.5°) or real-world validation

## Slide 10
Delivery Summary
Phase A
Clean T0
(engine verified)
Phase B
Deformed T1-T5
(series generated)
Phase C
Validation
(2 validators, PASS)
Scripts: 3 main (engine, 2 validators) + plotter + cross-check | Data: T0-T5 JSON, validation CSV, series plot