## Slide 1
Tunnel Crown Settlement Validation Workflow
Blender ground truth → Regular clean → Raycast TLS → Step 6 accuracy check
Regular MAPE
1.15%
Raycast MAPE
2.315%
Measured point
Ch 52.0m
Main metric: Crown settlement / Lún đỉnh hầm
Dataset: curved railway tunnel T0–T5

## Slide 2
STEP 6 VALIDATION
Goal: validate the tool using known settlement
Create one controlled tunnel model in Blender.
Apply known crown settlement from T0 to T5.
Run Step 6 on generated point clouds.
Compare tool output with known ground truth.
Ground truth settlement at Crown / Ch 52.0m
T0 = 0 mm T1 = -10 mm T2 = -22 mm T3 = -38 mm T4 = -58 mm T5 = -80 mm
Because the true deformation is known, the measured tool error can be calculated directly.

## Slide 3
STEP 6 VALIDATION
Complete workflow: one model, three comparable versions
3D Blender model
Curved railway tunnel with real-scale components.
Ground truth
Known settlement values.
Same crown point
Crown / Ch 52.0m.
Regular clean
Direct clean lining export.
Raycast TLS
Simulated scanner noise and occlusion.
Step 6
Measure crown settlement.
Error
mm %
Error mm = Tool result − Ground truth
Error % = |Error mm| / |Ground truth| × 100

## Slide 4
STEP 6 VALIDATION
Why two generated datasets are needed
Regular clean dataset
Purpose: test the algorithm in ideal conditions. Data: clean lining surface, minimal noise, no scanner occlusion. Meaning: if this is wrong, the core measurement logic has a problem.
Raycast field-like TLS dataset
Purpose: test practical robustness. Data: simulated laser scan with station positions, noise, dropout and occlusion. Meaning: this better represents real field scanning.
Both branches are compared against the same Blender ground truth.

## Slide 5
STEP 6 VALIDATION
Step 6 measurement rule
Main metric
Crown
Location
Ch 52.0m
Epochs
T0–T5
Status
OK/Warn/Danger
Crown settlement = total settlement compared with T0.
New crown move = additional settlement compared with previous epoch.
M3C2/p95 are supplementary checks, not the final crown settlement result.
This keeps the UI, table, export and validation focused on one clear measurement.

## Slide 6
STEP 6 VALIDATION
Accuracy result: tool output vs ground truth
Time | GT | Regular | Raycast | Reg err | Ray err
T0 | 0.0 | 0 | 0 | - | -
T1 | -10.0 | -9.9 | -10.243 | 1.00% | 2.43%
T2 | -22.0 | -21.7 | -21.632 | 1.36% | 1.67%
T3 | -38.0 | -37.6 | -37.07 | 1.05% | 2.45%
T4 | -58.0 | -57.3 | -56.607 | 1.21% | 2.40%
T5 | -80.0 | -79.1 | -77.9 | 1.13% | 2.63%
Regular MAPE
1.15%
Raycast MAPE
2.315%
Regular is more accurate because the surface is clean. Raycast error is higher because it includes field-like scan effects.
Both still follow the same T0→T5 settlement trend, so Step 6 quantifies crown settlement reliably.
T0 is not used in MAPE because its ground truth is 0 mm.

## Slide 7
STEP 6 VALIDATION
Conclusion
The workflow validates Step 6 against a known Blender ground truth.
Clean data error
1.15%
Field-like error
2.315%
Measured at
Crown / Ch 52m
Regular clean validates the algorithm under ideal conditions.
Raycast TLS validates robustness under field-like scanning conditions.
Next step: test with real TLS scans and calibrate preprocessing.
Key message: Step 6 measures crown settlement accurately enough for controlled validation.