## Slide 1
TLSynth Raycasting Protocol
Creating synthetic ground truth for tunnel deformation validation

## Slide 2
Purpose & Scope
1
• Create synthetic tunnel point clouds with KNOWN deformation
2
• Validate tunnel_analysis tool accuracy (mm-level precision)
3
• Follow TLSynth paper methodology (§3.1-3.5)
4
• Build confidence through 4 validation scenarios
5
• Ensure reproducibility and documentation
Notes: This protocol creates synthetic ground truth data using raycasting. We start with clean tunnel mesh, raycast to get T0 baseline, inject deformation, raycast again to get Tn, then validate tool accuracy.

## Slide 3
Key Concepts at a Glance
Raycasting
Virtual scanning: sphere shoots rays → hits tunnel → point cloud
Ground Truth
Exact, known deformation values injected into mesh
T0
Clean reference baseline (no deformation)
Tn
Monitoring scan with injected deformation
Validation
Compare tool output vs known ground truth
Notes: Understand core vocabulary: raycasting simulates laser scanning, ground truth is known deformation we inject, T0/Tn are temporal states, validation checks if tool measures them correctly.

## Slide 4
3-Phase Workflow
CLEAN MESH → Phase A: Raycast T0 → T0.las
↓
Phase B: Inject deformation
↓
Phase C: Raycast Tn → Tn.las
↓
VALIDATION: Compare vs Ground Truth
Phase A
T0 baseline
Phase B
Deformation
Phase C
Tn monitored
T0 raycast (15min) → Deform mesh (30min) → Tn raycast (15min) → Validate (30min)
Total: ~2 hours
Notes: Workflow is 3 phases plus validation. Phase A: clean baseline. Phase B: inject known deformation into mesh. Phase C: scan deformed mesh. Validation: load both into tool, compare measurements. Total ~2 hours.

## Slide 5
Phase A: Prepare T0 (Clean Reference)
• 1. Load tunnel mesh (16,100 vertices, Tunnel_Lining.blend)
• 2. Create scanner sphere @ position (0, 10, 3)
• 3. Raycast: fire 512 rays from sphere vertices
• 4. Add realistic noise: 5mm + 2mm per 10m distance
• 5. Export: T0.las (364 hit points)
• 6. Record metadata: radius (3.0m), eccentricity, ovality
Output: T0.las
~364 points | Radius: 3.0000m | e: 0.1mm | Clean, no deformation
Notes: Phase A creates the clean baseline. Load Blender tunnel mesh, create UV sphere at scanner location, raycast 512 rays, add realistic noise, export T0.las. Record metadata for comparison later.

## Slide 6
Phase B: Inject Deformation
Define ground truth deformation prescription:
Crown settlement: -7 mm @ chainage 20m
Sidewall convergence: -5 mm @ chainage 45m
Local damage: -15 mm @ chainage 65m
Modify tunnel mesh:
for vertex in mesh:
if at_chainage(20m): vertex.z -= 7mm # Crown down
if at_chainage(45m): vertex.xy *= 0.995 # Convergence
if at_chainage(65m): vertex.xyz -= 15mm # Damage
✓ Validate deformation on mesh ✓ Record ground_truth.csv
Notes: Phase B injects known deformation into tunnel mesh. Define exact amounts and locations (crown, convergence, damage). Modify vertices using Blender script or Python. Record all ground truth values before proceeding to Phase C.

## Slide 7
Phase C: Raycast Deformed Tunnel
CRITICAL: Use IDENTICAL scanner setup from Phase A
# Same scanner location & sphere subdivision
scanner_location = (0, 10, 3) # MUST match T0
scanner_sphere = UV_Sphere(subdivisions=32x16) # MUST match T0
# Load DEFORMED mesh (different from Phase A)
tunnel_mesh = load("tunnel_deformed.blend")
# Raycast with same noise model
for vertex in scanner_sphere:
hit = raycast(vertex, tunnel_mesh)
noise = 5 + (distance / 10) * 2 # Same noise as T0
Tn_points.append(hit + gaussian_noise)
export Tn.las
Output: Tn.las | Same point count as T0 | Deformation measurable
Notes: Phase C raycasts the deformed mesh using identical scanner setup. Only difference: target mesh changed to deformed version. Same scanner location, same ray count, same noise = differences are ONLY from deformation.

## Slide 8
Validation: Compare Measurements
• 1. Load T0.las into tunnel_analysis tool → get baseline metrics
• 2. Load Tn.las into tool → measure deformation
• 3. Tool reports: crown_settle, convergence, local_damage (mm)
• 4. Compare tool output vs ground_truth.csv
• 5. Calculate error: |measured - prescribed|
• 6. Assert: error < ±1mm → PASS ✓
✓ PASS: error < ±1mm
Tool is VALIDATED
✗ FAIL: error > ±5mm
Debug registration/noise
Notes: Load both scans into tool, measure deformation, compare vs ground truth. If error is small, tool is accurate. If large, debug the pipeline: check registration, noise level, fitting algorithm.

## Slide 9
Build Confidence: 4 Test Scenarios
A
No Deformation
T0 → T0. Expect: 0mm error.
B
Single Metric
Crown-only, convergence-only, damage-only.
C
Combined
All 3 deformations (realistic, stressful).
D
Offset Scanner
Different scanner location. Still measurable.
Record all results → validation_results.csv
Notes: Test protocol with 4 scenarios to build robustness. Scenario A: noise floor. Scenario B: isolated measurements. Scenario C: realistic stress test. Scenario D: generalization. Pass all 4 = confident validation.

## Slide 10
Implementation Timeline
Task
Duration
T0 raycast
15 min
Deform mesh (B1-B3)
30 min
Tn raycast
15 min
Load & validate tool
30 min
Error analysis
10 min
Repeat scenarios B,C,D
60 min (optional)
TOTAL
~2 hours (Scenarios A only)
Notes: Timeline to complete full protocol: ~2 hours for Scenario A baseline validation. Optional: repeat with scenarios B/C/D for additional robustness testing.

## Slide 11
Validation Metrics & Expected Accuracy
mm-Level Accuracy Target:
• Crown settlement: |measured - prescribed| < 1.0 mm
• Sidewall convergence: |measured - prescribed| < 1.0 mm
• Local damage: |measured - prescribed| < 2.0 mm
• Mean Absolute Error (MAE): < 0.6 mm (baseline from SSL T0→T5)
• Max error across all metrics: < 2.5 mm
✓ SUCCESS: If protocol achieves < ±1mm error
Tool is validated for mm-level deformation measurement
Notes: Accuracy target: mm-level precision. Crown and convergence < 1mm each. Damage < 2mm. Overall MAE < 0.6mm (historical baseline). Success = error < ±1mm for all metrics.

## Slide 12
Summary: What We Build
Deliverables:
• T0.las: Clean reference point cloud (364 points, no deformation)
• Tn.las: Deformed monitoring scan (known -7mm crown, -5mm convergence)
• ground_truth.csv: Prescribed deformation values
• validation_results.csv: Tool measurements vs ground truth
• Validation report: Error analysis and confidence metrics
Outcome: mm-level accuracy validation of tunnel_analysis tool
Based on TLSynth paper methodology + 2 hours of work
Notes: Final deliverables: T0.las, Tn.las, metadata, validation report. Outcome: tool validation at mm-level accuracy. Ready to deploy for field tunnel monitoring.