## Slide 1: Automated Point Cloud Analysis & Damage Inspection Tool
A Python-based solution for LiDAR data preprocessing & cross-section analysis
Presenter: Nguyen Duy Hoang Anh
Date: March 20, 2026
Smart Structure Lab (SSL) - CBNU

## Slide 2: Research Background & Objectives
Challenges with Osong Test Line Tunnel Data:
  Large-scale, noisy LiDAR point cloud data requires efficient preprocessing.
  Manual extraction of cross-sections and anomaly detection is highly inefficient.
Core Objectives:
  Automate 3D Point Cloud preprocessing (noise removal & outlier filtering).
  Establish an automatic cross-section extraction system based on reference lines.

## Slide 3: Tool Overview: Point Cloud Analysis v2.9
Platform: Python-based Desktop Application (GUI)
Core Technologies:
  Laspy & Open3D: High-speed 3D geometric processing.
  RANSAC Algorithm: Robust plane segmentation and normal vector analysis.
  Google Gemini LLM: Integrated AI agent for automated parameter tuning.
Dual-Mode Functionality: Tunnel/Corridor Analysis & Damage Inspection.

## Slide 4: Feature 1: Tunnel & Cross-Section Analysis
Automated Geometric Classification:
  Utilizes Iterative RANSAC to distinguish ground from wall structures.
Data Visualization & Analysis:
  3D Mesh Reconstruction from raw point clouds.
  Interactive 2D Slicing: Extract profiles at designated intervals along the Y-axis.
  Direct comparison with Design Profiles for construction error detection.

## Slide 5: Feature 2: Automated Damage Inspection
Quantitative Assessment of Deformation:
  Isolates the 'Main Surface' to establish a reference plane.
  Filters outliers representing structural variations (cracks, spalling, anomalies).
Automated Metric Extraction:
  Generates Bounding Boxes around damage clusters.
  Calculates approximate dimensions (L x W x H) of deformed regions.

## Slide 6: The 'Wow' Factor: AI Integration
Bridging the gap between Complex Algorithms and Field Usability:
AI Parameter Suggestion:
  Reads file headers (point count, density, bounds) to propose optimal RANSAC thresholds.
Automated Reporting:
  Synthesizes input parameters and geometric findings into formal technical summaries instantly.
Implements an automated analysis module to replace manual processing.

## Slide 7: Next Steps & Integration (2026 Roadmap)
Immediate Need:
  Require LiDAR Sample Data (Tunnel/Deformed surfaces) to validate noise filtering algorithms.
Virtual Environment Integration:
  Utilize cleaned data from this tool as input for Blender-based virtual tunnel construction.
  Simulate deformation scenarios in Blender and perform quantitative assessment using this tool.